## Slide 1: Lec??-ULTSEN-RASPBRY-HL-PR-2018-9-12.ppt
ULTSEN to RASPBRY-PI Connection
CTI One Corporation
Version: x0.1
Date: September 2018
Project Lead: Harry Li, Ph.D.
Team member: Prashanth Rajasekar
Company confidential

## Slide 2: ULTRASOUND Sensor working details
5V
GPIO#
GPIO#
GND
TRANSMITTER
RECEIVER
OBJECT
Original TRIGGER Wave
Reflected ECHO Wave
Range : 2cm to 4m
sound wave frequency
greater than 20,000 Hz

## Slide 3: Ultsen Raspberry_Pi Working Theory
Raspberry pi 3 Model B has a 4 core 1.2GHz CPU.
It is capable of performing 4 sensor tasks parallelly.
Currently we are connecting 3 Ultrasound sensors to Raspberry pi 3 B.
Raspberry pi 3 B will use its 3 cores to handle the 3 sensors.
Raspberry pi 3 B has sufficient RAM (1GB) to host the processes.
Multithreading concepts introduced to handle the 3 sensors parallelly.
Parallel data collection and conversion is done to calculate the distance wherever the sensor is being mounted.
According to the distance calculated, respective commands can be sent to the motor drive to take precautionary
steps.

## Slide 4: Raspberry Pi 3 System/Pin Details
CPU : 4× ARM Cortex-A53,
1.2GHz.
Technical Specification
CORES : 4
RAM : 1GB
GPIO : 40 Pin Headers
Storage : SD Card
Bluetooth : Bluetooth 4.1
26 GPIO Pins Available
No ADC Pins Available

## Slide 5: Ultsen Raspberry_Pi Pin Connections/Table
GND
GPIO 17
VCC
GPIO 4
VCC
VCC
GPIO 19
GPIO 26
GND
GPIO 27
GPIO 22
GND
S1
S2
S4
VCC
GND
GPIO 5
GPIO 6
VCC
GND
GPIO 23
GPIO 24
VCC
GND
GPIO 20
GPIO 21
S5
S6
S3

## Slide 6: Ultsen Raspberry_Pi Pin Connectivity Tables
ULTSEN 1 | RASP-PI
VCC | 5V
Trig | GPIO 4
Echo | GPIO 17
GND | GND
ULTSEN 2 | RASP-PI
VCC | 5V
Trig | GPIO 27
Echo | GPIO 22
GND | GND
ULTSEN 3 | RASP-PI
VCC | 5V
Trig | GPIO 5
Echo | GPIO 6
GND | GND
ULTSEN 4 | RASP-PI
VCC | 5V
Trig | GPIO 19
Echo | GPIO 26
GND | GND
ULTSEN 5 | RASP_PI
VCC | 5V
Trig | GPIO 23
Echo | GPIO 24
GND | GND
ULTSEN 6 | RASP-PI
VCC | 5V
Trig | GPIO 20
Echo | GPIO 21
GND | GND

## Slide 7: Ultsen Raspberry_Pi Circuit Diagram
GND
1.5K ohm
3K ohm
VCC
TRIG
ECHO
GND
3.2 V
Max GPIO input voltage=3.3 V

## Slide 8: Ultsen Raspberry_Pi Code Snippet
. . . . . . . . . function definition here.
Pin Declaration done here.
Pins Setup done here.
……… Thread 1 starts here.
……… Thread 2 starts here.
……… Thread 3 starts here.